## Slide 1: CS7290 Project Load/Store dependency prediction
Mentor: Pranith Kumar
Students: Kanghong Yan, Hanning Chen, Jiong Feng

## Slide 2: Motivation
The advances in core performance have outpaced the advances in memory subsystem performance over the previous decade.
Avoiding the processor to be stalled by the memory subsystem contributes a lot to performance in overall.
Modern processor speculatively issues multiple independent memory accesses to improve memory level parallelism (MLP) to mitigate stalls effect from the memory delay.

## Slide 3: Motivation
Speculative problem: dependent memory instructions, store-load dependencies causing RAW hazard, need to be serialized
  Causes pipeline flushing when they are speculatively executed.
This dependency can be dynamic based on the memory access pattern in a program. Detecting and predicting this dependency accurately helps avoid the pipeline flush overhead.

## Slide 4: idea
Utilize machine learning methodology to gain insights and find solution to the load/store dependency problem
Memory access streams can be viewed as a sequence
  Try recurrent neural network/transfomer to solve this problem
Propose a model to make future predictions of possible store-load dependencies.
We will use these predictions to achieve better performance by extending a store-sets based dependency predictor.

## Slide 5: Previous Work
ML/DL in computer architecture:
  Accelerator: (tons of )
    ASIC, FPGA, Processing In Memory (PIM)
    Translation between pipeline processor and neural network accelerator
  Using ML/DL to optimize computer architecture: (very little)
    Hardware prediction using simpler learning techniques like perceptron
    Machine Learning added NoC design
    …..
Difficulties for using ML/DL in computer architecture:
  Too much time and resource for training
  Hyperparameter tuning is hard in ML/DL/RL not mention to plus hardware
  Hard to implement “AI model” on hardware with limited space, energy etc

## Slide 6: methodology
PyTorch for network architecture exploration
  Dataset generates from SPEC2017 traces from ChampSim
MacSim/GEM5 for hardware design evaluation
Complex “Model” offline, simple “model” online
  After analyzing data offline, we will improve online model with much less resources usage.

## Slide 7: Milestone
RNN Memory Dependency Model
(1-2 weeks):
We firstly design a RNN model to predict memory dependency for a give program.
Training and validation data comes from the traces of SPEC 2017.
RNN Model Analysis
(1 week):
Gain insights from visualizations and understand why model performs well.
Would be helpful to remove redundancy from our model and prepare us for the next step.
Practical Model for Hardware Implementation
(2-3 weeks)
Simplified the previous proposed RNN model and implement on MacSim or Gem5.
Evaluate the result and write the paper

## Slide 8: goal
Learn more about memory dependency
Interaction between processor and memory subsystem
Submit paper for HPCA

## Slide 9: Thank you

## Slide 10: appendix

## Slide 11
Instruction Window:
PC INST
1 LD A
2 ADD R1, R2, R3
3 ST B
4 ST C
5 LD C
6 SUB R1, R2, R3
7 ST B
8 LD A
9 LD B
Model input plan 1:
Unified memory access vector:
[1 3 4 5 7 8 9]
Model’s target/label represents the dependency w.r.t. latest LD in the current instruction window
Model output plan A: [chosen]
Same size as instruction window (dependency w.r.t. PC 9, aka the last load in IW):
[0 1 0 0 1 0 0]